## Slide 1
Using Skyline to Monitor Long-Term Performance Metrics of High-Resolution Mass Spectrometers
J. Will Thompson and M. Arthur Moseley
Duke Proteomics Core Facility
Skyline Users Meeting – ASMS 2012

## Slide 2: The Duke Proteomics Core Facility
Arthur Moseley, PhD, DPCF Director (2007)
Will Thompson, PhD, Senior Laboratory Administrator (2007)
Laura Dubois, BS, Laboratory Analyst II (2008)
Erik Soderblom, Laboratory Analyst II (2008)
Matt Foster, PhD, Assistant Research Professor - Pulmonology, 20% DPCF (2009)
Meredith Turner, BS, Research Technician II (2010)
Brenna Richardson, PhD, Laboratory Analyst II (2011)

## Slide 3: System Suitability: “The process of validating whether your system is acceptable for providing useful analytical data without any bias.”
Operational Qualification (OQ): “Establishing confidence that equipment and sub-systems are capable of consistently operating with established limits and tolerances.”
Performance Qualification (PQ): “Demonstrate compliance with all requirements…including tests designed to verify the satisfactory performance of the equipment.”
From the GLP world:
We know this is important, but how do we go about doing this for a proteomic analysis?

## Slide 4: What Metrics are Important?
http://peptide.nist.gov/software/nist_msqc_pipeline/NIST_MSQC_Pipeline.html

## Slide 5: What Type of Sample?
Single Peptide? Single Protein? Few Proteins? Lysate?
TIME
COST
CARRYOVER
REAGENT STABILITY
SENSITIVITY
RELEVANCE

## Slide 6: ABRF-Sponsored Longitudinal Variability Study (2012-2013)
http://www.abrf.org/ResearchGroups/Proteomics/Studies/ABRF2012.pdf

## Slide 7: So, Just Start Somewhere…
In 2007, the DPCF started using 50 fmol injections of yeast alcohol dehydrogenase (Waters MassPrep)
Primary check was mass accuracy and sequence coverage, using database search results
In May 2011 the DPCF started using Skyline to analyze and track SS data from our QToF instruments using a Full Scan MS2 method targeting 7 analytes

## Slide 8: Skyline Setup for Full Scan MS/MS Analysis
https://skyline.gs.washington.edu/labkey/wiki/home/software/Skyline/page.view?name=tutorial_targeted_msms

## Slide 9: Targeted MS/MS (Pseudo-MRM) Method on a QToF

## Slide 10: Acquisition Method Details, Continued…

## Slide 11: Example Raw Data 50 fmol ADH1_YEAST digest, Synapt G2 HDMS

## Slide 12: Skyline Customizable View

## Slide 13: Longitudinal Measurements over 1 Year

## Slide 14: Peak Intensity versus Sequence Coverage

## Slide 15: LC Retention Time Consistency

## Slide 16: Other Chromatography Metrics
Average Peak Widths (with CV)
Average Retention Time (with CV)

## Slide 17: MS/MS Fragmentation Consistency

## Slide 18: Example of Precursor and Product Ion Extraction in Skyline, Ion Mobility-Data Independent Acquisition

## Slide 19: Summarization
Skyline provides a fast, efficient way to gain many system suitability metrics from most MS raw data formats
  Thermo, Waters, AB/Sciex, and Agilent
Easy to visualize performance over time, with data at the individual peptide or aggregate level
Can utilize Full Scan MS1, MS/MS, MRM, or DIA approaches for system suitability
Ability to set/visualize “thresholds” for performance metrics once they are established would be a plus