## Slide 1: Discovery to Targets for a Phosphoproteomic Signature Assay: One-stop shopping in Skyline
Jake Jaffe
Skyline Users Meeting
June 2013

## Slide 2: Idea: Phosphosignaling is coordinated!
Phosphosignaling is likely coordinated
  Kinase-substrate relationships tend to be 1-to-many
  A priori expectation of coordinate regulation of sites
Don’t need to monitor every phosphosite
Can we identify a few that we can reliably monitor?
  Go wide instead of deep

## Slide 3
Sites
Treatments/Cell lines
Largest systematic set of perturbations with phosphoproteomics readout in existence
  Over 10,000 phosphosites observed
Over 1,200 sites present in >75% of all experiments
Jinal Patel, Xiaodong Lu
‘Light’ Cells
‘Heavy’ Cells
‘Medium’ Cells
Control DMSO
Tx 1
Tx 2
MCF7
PC3
HL60
X
X
26
drugs
2
repeats
=

## Slide 4
Dimensionality reduction: >1000 to 55 with 2x probe redundancy
Roger Hu

## Slide 5: Now for the hard part… Building the P100 Assay

## Slide 6: Optimal Phosphosite Quant Requires Multiple Inputs
Level of phosphopeptide
  Picked “best” representative peptides from each cluster
    Observability, site localization, etc.
Level of non-phosphophorylated cognate
  Picked based on above
Level of a non-involved peptide
  Control for protein level
  Gleaned from all in-house MaxQuant data

## Slide 7: Assay Optimization Strategy
Identify and order peptides
Configure Skyline document
  Sequence identities
  Spectra libraries
Characterize peptides
  QC + establish RT properties
Refine spectral libraries
Configure final assay

## Slide 8: Step 1: Get Sequences into Skyline
Peptide shorthand makes it easy to insert modified sequences
  Make sure modifications are present in document!

## Slide 9: Entire assay document configured in one fell swoop

## Slide 10: Discovery and Targeted Platforms are Different
X
MaxQuant
  Used for all discovery data processing
  Performed all SILAC quantification
  MEGA result file
    MS/MS table (txt)
    2.8 GB
Skyline
  Targeted proteomics environment of choice
  Now supports MaxQuant / Andromeda formats

## Slide 11: Skyline Spectral Library Building

## Slide 12: Easily done even when data are distributed

## Slide 13: Instant Focused Spectral Library from > 2.8Gb Raw Spectra

## Slide 14: Peptide QC and RT Establishment
Run mixtures of peptides conforming to analysis clusters
  QExactive MS
  Inclusion lists pulled from Skyline doc
  Unscheduled…but fully targeted
Full-scan hi-res MS enables proof positive ID
  Allows comparison to library as a whole spectrum
  Mass accuracy increases confidence
  Can observe potential interferents when porting to triple quad

## Slide 15: Full-scan QC allows for proof-positive refinement

## Slide 16: Assay Optimization Strategy Revisited
Identify and order peptides
Configure Skyline document
  Sequence identities
  Spectra libraries
Characterize peptides
  QC + establish RT properties
  Will later use iRT strategy for assay scheduling
Refine spectral libraries
Configure final assay

## Slide 17: Distribution of the assay with Panorama
All of our work will be available to other labs
  To implement the assay at multiple sites
Ensure data analysis consistency
Clearing house of assay data
Communication with other project data infrastructures

## Slide 18: Conclusions
Skyline has contributed immensely to rapid configuration of our assay:
  Easy sequence import – even for modified peptides
  Easy spectral library creation based on discovery data
  Helpful in validation of synthetic peptides
  Sets groundwork for scheduling targeted assays
  Makes assay portable
  Panorama extension will make assay distributable
Feedback / support cycle of Skyline development can drive projects in real time

## Slide 19: Acknowledgements
LINCS Program and Program Officers
  U01 CA164186-01/Jaffe
MacCoss Lab, Univ. of Washington
  Mike MacCoss – co-PI
  Brendan MacLean
  Kaipo Tamura
  Vagisha Sharma
Broad Institute Proteomics Platform
  Jinal Patel
  Susan Abbatiello
  Lindsay Pino
  Philipp Mertins
  Steve Carr
Broad Institute LINCS Centers
  Todd Golub
  Aravind Subramanian
  Xiaodong Lu
  Roger Hu